## Slide 1
Chapter 20
Network Layer:
Internet Protocol
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
20-1 INTERNETWORKING
In this section, we discuss internetworking, connecting networks together to make an internetwork or an internet.
Need for Network Layer Internet as a Datagram Network Internet as a Connectionless Network
Topics discussed in this section:

## Slide 3
Figure 20.1 Links between two hosts

## Slide 4
Figure 20.2 Network layer in an internetwork

## Slide 5
Figure 20.3 Network layer at the source, router, and destination

## Slide 6
Figure 20.3 Network layer at the source, router, and destination (continued)

## Slide 7
Switching at the network layer in the Internet uses the datagram approach to packet switching.
Note

## Slide 8
Communication at the network layer in the Internet is connectionless.
Note

## Slide 9
20-2 IPv4
The Internet Protocol version 4 (IPv4) is the delivery mechanism used by the TCP/IP protocols.
Datagram Fragmentation Checksum
Options
Topics discussed in this section:

## Slide 10
Figure 20.4 Position of IPv4 in TCP/IP protocol suite

## Slide 11
Figure 20.5 IPv4 datagram format

## Slide 12
Figure 20.6 Service type or differentiated services

## Slide 13
The precedence subfield was part of version 4, but never used.
Note

## Slide 14
Table 20.1 Types of service

## Slide 15
Table 20.2 Default types of service

## Slide 16
Table 20.3 Values for codepoints

## Slide 17
The total length field defines the total length of the datagram including the header.
Note

## Slide 18
Figure 20.7 Encapsulation of a small datagram in an Ethernet frame

## Slide 19
Figure 20.8 Protocol field and encapsulated data

## Slide 20
Table 20.4 Protocol values

## Slide 21
An IPv4 packet has arrived with the first 8 bits as shown:
01000010
The receiver discards the packet. Why?
Solution
There is an error in this packet. The 4 leftmost bits (0100) show the version, which is correct. The next 4 bits (0010) show an invalid header length (2 × 4 = 8). The minimum number of bytes in the header must be 20. The packet has been corrupted in transmission.
Example 20.1

## Slide 22
In an IPv4 packet, the value of HLEN is 1000 in binary. How many bytes of options are being carried by this packet?
Solution
The HLEN value is 8, which means the total number of bytes in the header is 8 × 4, or 32 bytes. The first 20 bytes are the base header, the next 12 bytes are the options.
Example 20.2

## Slide 23
In an IPv4 packet, the value of HLEN is 5, and the value of the total length field is 0x0028. How many bytes of data are being carried by this packet?
Solution
The HLEN value is 5, which means the total number of bytes in the header is 5 × 4, or 20 bytes (no options). The total length is 40 bytes, which means the packet is carrying 20 bytes of data (40 − 20).
Example 20.3

## Slide 24
An IPv4 packet has arrived with the first few hexadecimal digits as shown.
0x45000028000100000102 . . .
How many hops can this packet travel before being dropped? The data belong to what upper-layer protocol?
Solution
To find the time-to-live field, we skip 8 bytes. The time-to-live field is the ninth byte, which is 01. This means the packet can travel only one hop. The protocol field is the next byte (02), which means that the upper-layer protocol is IGMP.
Example 20.4

## Slide 25
Figure 20.9 Maximum transfer unit (MTU)

## Slide 26
Table 20.5 MTUs for some networks

## Slide 27
Figure 20.10 Flags used in fragmentation

## Slide 28
Figure 20.11 Fragmentation example

## Slide 29
Figure 20.12 Detailed fragmentation example

## Slide 30
A packet has arrived with an M bit value of 0. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?
Solution
If the M bit is 0, it means that there are no more fragments; the fragment is the last one. However, we cannot say if the original packet was fragmented or not. A non-fragmented packet is considered the last fragment.
Example 20.5

## Slide 31
A packet has arrived with an M bit value of 1. Is this the first fragment, the last fragment, or a middle fragment? Do we know if the packet was fragmented?
Solution
If the M bit is 1, it means that there is at least one more fragment. This fragment can be the first one or a middle one, but not the last one. We don’t know if it is the first one or a middle one; we need more information (the value of the fragmentation offset).
Example 20.6

## Slide 32
A packet has arrived with an M bit value of 1 and a fragmentation offset value of 0. Is this the first fragment, the last fragment, or a middle fragment?
Solution
Because the M bit is 1, it is either the first fragment or a middle one. Because the offset value is 0, it is the first fragment.
Example 20.7

## Slide 33
A packet has arrived in which the offset value is 100. What is the number of the first byte? Do we know the number of the last byte?
Solution
To find the number of the first byte, we multiply the offset value by 8. This means that the first byte number is 800. We cannot determine the number of the last byte unless we know the length.
Example 20.8

## Slide 34
A packet has arrived in which the offset value is 100, the value of HLEN is 5, and the value of the total length field is 100. What are the numbers of the first byte and the last byte?
Solution
The first byte number is 100 × 8 = 800. The total length is 100 bytes, and the header length is 20 bytes (5 × 4), which means that there are 80 bytes in this datagram. If the first byte number is 800, the last byte number must be 879.
Example 20.9

## Slide 35
Figure 20.13 shows an example of a checksum calculation for an IPv4 header without options. The header is divided into 16-bit sections. All the sections are added and the sum is complemented. The result is inserted in the checksum field.
Example 20.10

## Slide 36
Figure 20.13 Example of checksum calculation in IPv4

## Slide 37
Figure 20.14 Taxonomy of options in IPv4

## Slide 38
20-3 IPv6
The network layer protocol in the TCP/IP protocol suite is currently IPv4. Although IPv4 is well designed, data communication has evolved since the inception of IPv4 in the 1970s. IPv4 has some deficiencies that make it unsuitable for the fast-growing Internet.
Advantages Packet Format Extension Headers
Topics discussed in this section:

## Slide 39
Figure 20.15 IPv6 datagram header and payload

## Slide 40
Figure 20.16 Format of an IPv6 datagram

## Slide 41
Table 20.6 Next header codes for IPv6

## Slide 42
Table 20.7 Priorities for congestion-controlled traffic

## Slide 43
Table 20.8 Priorities for noncongestion-controlled traffic

## Slide 44
Table 20.9 Comparison between IPv4 and IPv6 packet headers

## Slide 45
Figure 20.17 Extension header types

## Slide 46
Table 20.10 Comparison between IPv4 options and IPv6 extension headers

## Slide 47
20-4 TRANSITION FROM IPv4 TO IPv6
Because of the huge number of systems on the Internet, the transition from IPv4 to IPv6 cannot happen suddenly. It takes a considerable amount of time before every system in the Internet can move from IPv4 to IPv6. The transition must be smooth to prevent any problems between IPv4 and IPv6 systems.
Dual Stack Tunneling Header Translation
Topics discussed in this section:

## Slide 48
Figure 20.18 Three transition strategies

## Slide 49
Figure 20.19 Dual stack

## Slide 50
Figure 20.20 Tunneling strategy

## Slide 51
Figure 20.21 Header translation strategy

## Slide 52
Table 20.11 Header translation