## Slide 1
Chapter 21
Network Layer: Address Mapping,
Error Reporting, and Multicasting
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
21-1 ADDRESS MAPPING
The delivery of a packet to a host or a router requires two levels of addressing: logical and physical. We need to be able to map a logical address to its corresponding
physical address and vice versa. This can be done by using either static or dynamic mapping.
Mapping Logical to Physical Address
Mapping Physical to Logical Address
Topics discussed in this section:

## Slide 3
Figure 21.1 ARP operation

## Slide 4
Figure 21.2 ARP packet

## Slide 5
Figure 21.3 Encapsulation of ARP packet

## Slide 6
Figure 21.4 Four cases using ARP

## Slide 7
An ARP request is broadcast; an ARP reply is unicast.
Note

## Slide 8
A host with IP address 130.23.43.20 and physical address B2:34:55:10:22:10 has a packet to send to another host with IP address 130.23.43.25 and physical address A4:6E:F4:59:83:AB. The two hosts are on the same Ethernet network. Show the ARP request and reply packets encapsulated in Ethernet frames.
Solution
Figure 21.5 shows the ARP request and reply packets. Note that the ARP data field in this case is 28 bytes, and that the individual addresses do not fit in the 4-byte boundary. That is why we do not show the regular 4-byte boundaries for these addresses.
Example 21.1

## Slide 9
Figure 21.5 Example 21.1, an ARP request and reply

## Slide 10
Figure 21.6 Proxy ARP

## Slide 11
Figure 21.7 BOOTP client and server on the same and different networks

## Slide 12
DHCP provides static and dynamic address allocation that can be manual or automatic.
Note

## Slide 13
21-2 ICMP
The IP protocol has no error-reporting or error-correcting mechanism. The IP protocol also lacks a mechanism for host and management queries. The Internet Control Message Protocol (ICMP) has been designed to compensate for the above two deficiencies. It is a companion to the IP protocol.
Types of Messages Message Format Error Reporting and Query
Debugging Tools
Topics discussed in this section:

## Slide 14
Figure 21.8 General format of ICMP messages

## Slide 15
ICMP always reports error messages to the original source.
Note

## Slide 16
Figure 21.9 Error-reporting messages

## Slide 17
Important points about ICMP error messages:
❏ No ICMP error message will be generated in response to a datagram carrying an ICMP error message.
❏ No ICMP error message will be generated for a fragmented datagram that is not the first fragment.
❏ No ICMP error message will be generated for a datagram having a multicast address.
❏ No ICMP error message will be generated for a datagram having a special address such as 127.0.0.0 or 0.0.0.0.
Note

## Slide 18
Figure 21.10 Contents of data field for the error messages

## Slide 19
Figure 21.11 Redirection concept

## Slide 20
Figure 21.12 Query messages

## Slide 21
Figure 21.13 Encapsulation of ICMP query messages

## Slide 22
Figure 21.14 shows an example of checksum calculation for a simple echo-request message. We randomly chose the identifier to be 1 and the sequence number to be 9. The message is divided into 16-bit (2-byte) words. The words are added and the sum is complemented. Now the sender can put this value in the checksum field.
Example 21.2

## Slide 23
Figure 21.14 Example of checksum calculation

## Slide 24
We use the ping program to test the server fhda.edu. The result is shown on the next slide. The ping program sends messages with sequence numbers starting from 0. For each probe it gives us the RTT time. The TTL (time to live) field in the IP datagram that encapsulates an ICMP
message has been set to 62. At the beginning, ping defines the number of data bytes as 56 and the total number of bytes as 84. It is obvious that if we add 8 bytes of ICMP header and 20 bytes of IP header to 56, the result is 84. However, note that in each probe ping defines the number of bytes as 64. This is the total number of bytes in the ICMP packet (56 + 8).
Example 21.3

## Slide 25
Example 21.3 (continued)

## Slide 26
Figure 21.15 The traceroute program operation

## Slide 27
We use the traceroute program to find the route from the computer voyager.deanza.edu to the server fhda.edu. The following shows the result:
Example 21.4
The unnumbered line after the command shows that the destination is 153.18.8.1. The packet contains 38 bytes: 20 bytes of IP header, 8 bytes of UDP header, and 10 bytes of application data. The application data are used by traceroute to keep track of the packets.

## Slide 28
The first line shows the first router visited. The router is named Dcore.fhda.edu with IP address 153.18.31.254. The first round-trip time was 0.995 ms, the second was 0.899 ms, and the third was 0.878 ms. The second line shows the second router visited. The router is named Dbackup.fhda.edu with IP address 153.18.251.4. The three round-trip times are also shown. The third line shows the destination host. We know that this is the destination host because there are no more lines. The destination host is the server fhda.edu, but it is named tiptoe.fhda.edu with the IP address 153.18.8.1. The three round-trip times are also shown.
Example 21.4 (continued)

## Slide 29
In this example, we trace a longer route, the route to xerox.com (see next slide). Here there are 17 hops between source and destination. Note that some round-trip times look unusual. It could be that a router was too busy to process the packet immediately.
Example 21.5

## Slide 30
Example 21.5 (continued)

## Slide 31
21-3 IGMP
The IP protocol can be involved in two types of communication: unicasting and multicasting. The Internet Group Management Protocol (IGMP) is one of the necessary, but not sufficient, protocols that is involved in multicasting. IGMP is a companion to the IP protocol.
Group Management IGMP Messages and IGMP Operation
Encapsulation
Netstat Utility
Topics discussed in this section:

## Slide 32
Figure 21.16 IGMP message types

## Slide 33
Figure 21.17 IGMP message format

## Slide 34
Table 21.1 IGMP type field

## Slide 35
Figure 21.18 IGMP operation

## Slide 36
In IGMP, a membership report is sent twice, one after the other.
Note

## Slide 37
The general query message does not define a particular group.
Note

## Slide 38
Imagine there are three hosts in a network, as shown in Figure 21.19. A query message was received at time 0; the random delay time (in tenths of seconds) for each group is shown next to the group address. Show the sequence of report messages.
Example 21.6
Solution
The events occur in this sequence:
a. Time 12: The timer for 228.42.0.0 in host A expires, and a membership report is sent, which is received by the router and every host including host B which cancels its timer for 228.42.0.0.

## Slide 39
Example 21.6 (continued)
b. Time 30: The timer for 225.14.0.0 in host A expires, and a membership report is sent which is received by the router and every host including host C which cancels its timer for 225.14.0.0.
c. Time 50: The timer for 238.71.0.0 in host B expires, and a membership report is sent, which is received by the router and every host.
d. Time 70: The timer for 230.43.0.0 in host C expires, and a membership report is sent, which is received by the router and every host including host A which cancels its timer for 230.43.0.0.

## Slide 40
Figure 21.19 Example 21.6

## Slide 41
Figure 21.20 Encapsulation of IGMP packet

## Slide 42
The IP packet that carries an IGMP packet has a value of 1 in its TTL field.
Note

## Slide 43
Table 21.2 Destination IP addresses

## Slide 44
Figure 21.21 Mapping class D to Ethernet physical address

## Slide 45
An Ethernet multicast physical address is in the range
01:00:5E:00:00:00 to 01:00:5E:7F:FF:FF.
Note

## Slide 46
Change the multicast IP address 230.43.14.7 to an Ethernet multicast physical address.
Solution
We can do this in two steps:
a. We write the rightmost 23 bits of the IP address in hexadecimal. This can be done by changing the rightmost 3 bytes to hexadecimal and then subtracting 8 from the leftmost digit if it is greater than or equal to 8. In our example, the result is 2B:0E:07.
Example 21.7

## Slide 47
b. We add the result of part a to the starting Ethernet multicast address, which is 01:00:5E:00:00:00. The result is
Example 21.7 (continued)

## Slide 48
Change the multicast IP address 238.212.24.9 to an Ethernet multicast address.
Solution
a. The rightmost 3 bytes in hexadecimal is D4:18:09. We need to subtract 8 from the leftmost digit, resulting in 54:18:09.
Example 21.8
b. We add the result of part a to the Ethernet multicast starting address. The result is

## Slide 49
Figure 21.22 Tunneling

## Slide 50
We use netstat (see next slide) with three options: -n, -r, and -a. The -n option gives the numeric versions of IP addresses, the -r option gives the routing table, and the -a option gives all addresses (unicast and multicast). Note that we show only the fields relative to our discussion. “Gateway” defines the router, “Iface” defines the interface.
Note that the multicast address is shown in color. Any packet with a multicast address from 224.0.0.0 to 239.255.255.255 is masked and delivered to the Ethernet interface.
Example 21.9

## Slide 51
Example 21.9 (continued)

## Slide 52
21-4 ICMPv6
We discussed IPv6 in Chapter 20. Another protocol that has been modified in version 6 of the TCP/IP protocol suite is ICMP (ICMPv6). This new version follows the same strategy and purposes of version 4.
Error Reporting
Query
Topics discussed in this section:

## Slide 53
Figure 21.23 Comparison of network layers in version 4 and version 6

## Slide 54
Table 21.3 Comparison of error-reporting messages in ICMPv4 and ICMPv6

## Slide 55
Table 21.4 Comparison of query messages in ICMPv4 and ICMPv6