## Slide 1
Chapter 29
Multimedia
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
Figure 29.1 Internet audio/video

## Slide 3
Streaming stored audio/video refers to on-demand requests for compressed audio/video files.
Note

## Slide 4
Streaming live audio/video refers to the broadcasting of radio and TV programs through the Internet.
Note

## Slide 5
Interactive audio/video refers to the use of the Internet for interactive audio/video applications.
Note

## Slide 6
29-1 DIGITIZING AUDIO AND VIDEO
Before audio or video signals can be sent on the Internet, they need to be digitized. We discuss audio and video separately.
Digitizing Audio
Digitizing Video
Topics discussed in this section:

## Slide 7
Compression is needed to send video over the Internet.
Note

## Slide 8
29-2 AUDIO AND VIDEO COMPRESSION
To send audio or video over the Internet requires compression. In this section, we discuss audio compression first and then video compression.
Audio Compression Video Compression
Topics discussed in this section:

## Slide 9
Figure 29.2 JPEG gray scale

## Slide 10
Figure 29.3 JPEG process

## Slide 11
Figure 29.4 Case 1: uniform gray scale

## Slide 12
Figure 29.5 Case 2: two sections

## Slide 13
Figure 29.6 Case 3: gradient gray scale

## Slide 14
Figure 29.7 Reading the table

## Slide 15
Figure 29.8 MPEG frames

## Slide 16
Figure 29.9 MPEG frame construction

## Slide 17
29-3 STREAMING STORED AUDIO/VIDEO
Now that we have discussed digitizing and compressing audio/video, we turn our attention to specific applications. The first is streaming stored audio and video.
First Approach: Using a Web Server Second Approach: Using a Web Server with a Metafile Third Approach: Using a Media Server Fourth Approach: Using a Media Server and RTSP
Topics discussed in this section:

## Slide 18
Figure 29.10 Using a Web server

## Slide 19
Figure 29.11 Using a Web server with a metafile

## Slide 20
Figure 29.12 Using a media server

## Slide 21
Figure 29.13 Using a media server and RTSP

## Slide 22
29-4 STREAMING LIVE AUDIO/VIDEO
Streaming live audio/video is similar to the broadcasting of audio and video by radio and TV stations. Instead of broadcasting to the air, the stations broadcast through the Internet. There are several similarities between streaming stored audio/video and
streaming live audio/video. They are both sensitive to delay; neither can accept retransmission. However, there is a difference. In the first application, the communication is unicast and on-demand. In the second, the communication is multicast and live.

## Slide 23
29-5 REAL-TIME INTERACTIVE AUDIO/VIDEO
In real-time interactive audio/video, people communicate with one another in real time. The Internet phone or voice over IP is an example of this type of application. Video conferencing is another example that allows people to communicate visually and orally.
Characteristics
Topics discussed in this section:

## Slide 24
Figure 29.14 Time relationship

## Slide 25
Jitter is introduced in real-time data by the delay between packets.
Note

## Slide 26
Figure 29.15 Jitter

## Slide 27
Figure 29.16 Timestamp

## Slide 28
To prevent jitter, we can time-stamp the packets and separate the arrival time from the playback time.
Note

## Slide 29
Figure 29.17 Playback buffer

## Slide 30
A playback buffer is required for real-time traffic.
Note

## Slide 31
A sequence number on each packet is required for real-time traffic.
Note

## Slide 32
Real-time traffic needs the support of multicasting.
Note

## Slide 33
Translation means changing the encoding of a payload to a lower
quality to match the bandwidth
of the receiving network.
Note

## Slide 34
Mixing means combining several streams of traffic into one stream.
Note

## Slide 35
TCP, with all its sophistication, is not suitable for interactive multimedia
traffic because we cannot allow retransmission of packets.
Note

## Slide 36
UDP is more suitable than TCP for interactive traffic. However, we
need the services of RTP,
another transport layer
protocol, to make up
for the deficiencies
of UDP.
Note

## Slide 37
29-6 RTP
Real-time Transport Protocol (RTP) is the protocol designed to handle real-time traffic on the Internet. RTP does not have a delivery mechanism; it must be used with UDP. RTP stands between UDP and the application program. The main contributions of RTP are time-stamping, sequencing, and mixing facilities.
RTP Packet Format UDP Port
Topics discussed in this section:

## Slide 38
Figure 29.18 RTP

## Slide 39
Figure 29.19 RTP packet header format

## Slide 40
Table 20.1 Payload types

## Slide 41
RTP uses a temporary even-numbered UDP port.
Note

## Slide 42
29-7 RTCP
RTP allows only one type of message, one that carries data from the source to the destination. In many cases, there is a need for other messages in a session. These messages control the flow and quality of data and allow the recipient to send feedback to the source
or sources. Real-time Transport Control Protocol (RTCP) is a protocol designed for this purpose.
Sender Report and Receiver Report Messages UDP Port
Topics discussed in this section:

## Slide 43
Figure 29.20 RTCP message types

## Slide 44
RTCP uses an odd-numbered UDP port number that follows the port number selected for RTP.
Note

## Slide 45
29-8 VOICE OVER IP
Let us concentrate on one real-time interactive audio/video application: voice over IP, or Internet telephony. The idea is to use the Internet as a telephone network with some additional capabilities. Two protocols have been designed to handle this type of communication: SIP and H.323.
SIP H.323
Topics discussed in this section:

## Slide 46
Figure 29.21 SIP messages

## Slide 47
Figure 29.22 SIP formats

## Slide 48
Figure 29.23 SIP simple session

## Slide 49
Figure 29.24 Tracking the callee

## Slide 50
Figure 29.25 H.323 architecture

## Slide 51
Figure 29.26 H.323 protocols

## Slide 52
Figure 29.27 H.323 example